## Slide 1
Smart Charger For Electric Vehicles

## Slide 2
Team Members
Asmaa Anwer
Aya Ramzy

## Slide 3
Our Sponsors & Mentors
Supervised By:
Dr. Ali Rashed
Dr. Maha Medhat
Mentored By:
Eng. Ahmed Assaf
Eng. Alaa Nofal
Eng. Omar Mekkawy

## Slide 4
Our Thought During Idea Searching Phase(why)?
MARKET
SKILLS
CAREER
CAREER:
Our jobs requirements and meets our team intended learning objectives through graduation project.
SKILLS:
Choose idea which assembles different technical skills in our team.
MARKET:
Trend idea which is competitive and meets up to date market requirement.

## Slide 5
Problem Statement

## Slide 6
Software Block Diagram
STK
APP
ADC
USART
STK
TEMP
DIO
VOLT
ADC
DIO
RCC
RCC
CURRENT
RCC
ADC
TFT
DIO
SPI
RCC
ESP
USART
DIO
RCC
DIO
DIO
RCC
PWM
RELAY
RCC
USART
DIO
APP
APP
Charger ECU
Car ECU

## Slide 7
Files And Naming Convention
Files Division Rules
ModuleName_private.h
Module
ModuleName_Interface.h
ModuleName_Config.h
ModuleName_Program.c
Implementation of the Functions
Configuration parameters that the user should select it
Definition of the APIs that another modules use it
Registers definition , Pins definitions

## Slide 8
Detailed Design
Module | APIs | Description
ESP | void ESP_u8Init(void); | Its an initialization function that init the esp wifi module - It takes void and return void
 | u8 ESP_u8ConnectAP(u8*SSIDName, u8* SSIDPass ) ; | Its an interface function , another modules can use it to connect wifi with the internet It takes the network name and password and returns u8
 | u8 ESP_u8ConnectServer(u8* ip); | Its an interface function , another modules can use it to connect wifi with the Server It takes the IP of the server and returns u8

## Slide 9
Module | APIs | Description
ESP | Void ESP8266_VoidSendHttpReq( u8 * Copy_u8Key , u8 *Copy_u8Data , u8 *Copy_u8Length , u8 *field ); | Its an interface function , another modules can use it to send data to the internet It takes key of the channel , data the will be sent , Length of the URL , Field that the data will sent to it .

## Slide 10
Detailed Design
Module | APIs | Description
TFT | void TFT_voidInit (void); | Its an initialization function that init the Initialize TFT module - It takes void and return void
 | void TFT_voidPrintText(s8 *copy_s8Text , u16 copy_u16X , u16 copy_u16Y, u8 copy_u8Size , u16 copy_u16Color , u16 copy_u16BackColor); | Its an interface function , another modules can use it to print text on the TFT It takes the text that will be displayed , its place (x ,y ) , Size of text , text colour and back ground colour .
 | void TFT_voidPrintChar(s8 copy_s8Char , u16 copy_u16X , u16 copy_u16Y, u8 copy_u8Size , u16 copy_u16Color, u16 copy_u16BackColor); | Its an interface function , another modules can use it to Print character on the display It takes the Char that will be displayed , its place (x ,y ) , Size of text , text colour and back ground colour

## Slide 11
Detailed Design
Module | APIs | Description
USART | void USART_voidInit(sUART_Config_t *UART_Config); | Its an initialization function that init the Initialize USART module - It takes struct that hold the USART config and return void
 | void USART_voidSendCharSynch( eUSART_Num_t USART_Number, u8 copy_u8Char); | Its an interface function , another modules can use it to send character using uart It takes the UART that will send the data , character that will be sent
 | u8 USART_u8ReceiveCharSynch( eUSART_Num_t USART_Number) ; | Its an interface function , another modules can use it to receive char It returns the character , takes the UART that will receive the data

## Slide 12
Module | APIs | Description
USART | void USART_voidSendStringSynch( eUSART_Num_t USART_Number, u8 * Pu8Char); | Its an interface function , another modules can use it to send String using uart It takes the UART that will send the data , Text that will be sent
 | void USART_voidReceiveStringSynch(eUSART_Num_t USART_Number, u8 * Pu8String); | Its an interface function , another modules can use it to receive Text It takes the UART that will receive the data , pointer that will hold the string .
Detailed Design

## Slide 13
Detailed Design
Module | APIs | Description
SPI | u8 SPI_u8ConfigureCh(SPI_Ch_t copy_channel , SPI_config_t *copy_config) | Its an initialization function that init the Initialize SPI module - It takes struct that hold the SPI config and SPI that will send data
 | u16 SPI_voidSendRecSynch (SPI_Ch_t copy_channel , u16 copy_u16SendData) | Its an interface function , another modules can use it to send character and receive data using SPI It takes the SPI that will send the data , DATA that will be sent
 | void SPI_voidSendRecAsynch (SPI_Ch_t copy_channel , u16 copy_u16SendData , void (*func)(u16)) ; | Its an interface function , another modules can use it to send character and receive data using SPI but using interrupt It takes the SPI that will send the data , DATA that will be sent , and pointer to a function .